## Slide 1: Work flow: Generation of ANN Database and ANN training

## Slide 2: 1. Step: Read in Raw data
Read in the raw data of different TNF ESF simulations
This is done with TNF_datareader.py
Currently the following time steps have been used:
cases_SuperMUC = ['case-05_ESF_linear','case-05', 'case-05_lam_lowMa', 'case-05_lowT_lam','case-05_lam_lowMa_4Ord',
'case-44_react_lam_WALE','case-42_react_ESF_WALE_1Mio']
cases_Cluster=['case-27_lam_WALE_2.8Mio_linear','case-43_ESF_WALE_2.8Mio','case-43_ESF_WALE_2.8Mio_linear','case-46_lam_WALE_550k_Pr0.2']
The species mass fractions, temperature and pressure are then stored in a hdf5 format, named: 'TNF_states.h5‘
Important: Only data between 0.001 < f_Bilger < 0.4 will be stored! However, some values outside this range are included, depending on e.g. sample_size=10000
It is not clear if these are needed for the training process!

## Slide 3: 2. Step: ODE Integration
Use the database: 'TNF_states.h5‘, with key is 'TNF_raw_data'
and generate ODE integrated reaction rates. This is done with Cantera_ODE_TNF.py
It does the following:
Loop over all database entries
Compute RR of all species with Cantera and Lu19 mechanism if Temperature is above a criteria, e.g. remove_T_below=310
The reaction Rate RR is defined as RR = (Y_now – Y_before)*rho/ time_step
You need to specify the time step in self.dt, usually 1e-7 is ok.
A new database will be created: 'TNF_integrated_dt1e-7.h5‘, it contains:
Species before
Species after
T before
T after
RR_Y
dt is only saved in the name of the database
Key is 'TNF_data_integrated'

## Slide 4: 3. Step: Filter and shuffle the data base
The data base 'TNF_integrated_dt1e-7.h5‘ needs to be shuffled (rows) prior to any kind of batch training, as currently data is ordered the way it was read in. This is done with TNF_shuffle_filter.py
Dask is used to read in the database. Based on a criteria, e.g. the minimal RR_CH4 reaction rate the data base is filtered. Means: only every 10th row where RR_CH4 is below a threshold is kept in the data set. Ideally, this should remove all data points where no reaction takes place, this should be the case for fully burnt or unburnt states – these need not to be learned.
Check carefully how to define the threshold, to avoid any bias in the training.

## Slide 5: Work flow: Generation of ANN Database